## Slide 1
HALO: Accelerating Flow Classification for Scalable Packet Processing in NFV
Yifan Yuan † Yipeng Wang Ren Wang Jian Huang †
†

## Slide 2
What is Network Function Virtualization (NFV)?
Network Functions
Access
Control List
Network Address
Translation
Domain Name System
Firewall
Intrusion Detection
Cloud Computing
Softwarization
(Virtualization)
Good Scalability, Flexible Deployment, and Reduced Operational Cost

## Slide 3
How to Deploy NFV?
Virtual switch is the key component of NFV platform.

## Slide 4
The Function of Virtual Switch: an Example
Key Functions: Match patterns, find rules, and forward packets.
A: 10.0.0.1
B: 10.0.0.11
C: 10.0.0.12
D: 10.0.0.13
?
Flow Table |  | 
Flow | Pattern | Action Rule
Flow 1 | Destination IP == 10.0.0.12 | Forward to D
Flow 2 | Destination IP == 10.0.0.11 | Forward to B
…… | …… | ……
Match
Packet
Source IP
10.0.0.1
Destination IP
10.0.0.11

## Slide 5
What Does a Real vSwitch Look Like?
Layered design with multiple hash tables for flow classification.
Hash tables (tuples)
?
Flow and
Rules
Packets

## Slide 6
Virtual Switch Performance Analysis
We set up a test platform with state-of-the-art hardware/software to profile the performance of Open vSwitch (OVS).
+
+
+
40GbE
NIC
+
Hardware
Traffic Generator

## Slide 7
Flow Classification is the Major Bottleneck
310 cyc/pkt
~70%!
Packet Processing Time Percentage
340 cyc/pkt
343
cyc/pkt
640 cyc/pkt
993 cyc/pkt
Flow classification in OVS suffers from significant performance overhead.
A series of hash-table lookups in one tuple space search, no parallelism

## Slide 8
Hash Table: Where Does the Overhead Come From
Hash table lookup requires many instructions, and
large portion of them are memory operations
Only 3 input/output: table address, key and result
Simple control flow
On average, ~210 instructions per lookup operation
~50% are load/store (most hit in Last Level Cache - LLC)

## Slide 9
Hash Table: Concurrency and Atomicity
Need low-cost atomicity guarantee for concurrent data structures.
Core-to-core communication
  5x slower than single-core communication
Read-write locking mechanism
  ~14% throughput drop with lock free design
Concurrent data structures are used to scale performance. BUT

## Slide 10
Design Overview
Virtual Switch
Overhead:
Hash-Table
Memory access
Many instructions
Concurrency
Observation
Large portion of useful data can reside in LLC
+
HALO:
Distributed
Near-Cache
Accelerators

## Slide 11
HALO : Hardware-Assisted LOokup
Light-weight Locking Mechanism
X86-64 Instruction Extension
Distributed Near-Data Accelerator
X86-64 Instruction Extension
Light-weight Locking Mechanism
Near data
Parallelism
Hw assisted
Low cost
All-in-one
Easy to use
Large portion of data in LLC
Too Many Instructions
Concurrency Overhead
Too Many Instructions
Large portion of data in LLC
Concurrency Overhead

## Slide 12
Distributed Near-Cache Accelerator
Near-cache: Faster data access
Distributed: explores parallelism for scalability
Caching and Home Agent:
Responsible for coherency protocol, data access, etc.
Common in Intel CPU.

## Slide 13
HALO : Hardware-Assisted LOokup
Light-weight Locking Mechanism
X86-64 Instruction Extension
Distributed Near-Data Accelerator
X86-64 Instruction Extension
Distributed Near-Data Accelerator
Useful Data in LLC
Too Many Instructions
Concurrency Overhead
Too Many Instructions
Useful Data in LLC
Concurrency Overhead

## Slide 14
Light-weight Locking Mechanism
Design: one “lock” bit in cache line’s metadata, to prevent writing thread moving data around while reading.
Fast (near data), fine-grained (per cache line) and low overhead (one bit).
X
HALO Read (lookup)
Write (cuckoo move)
Not atomic

## Slide 15
HALO : Hardware-Assisted LOokup
Light-weight Locking Mechanism
X86-64 Instruction Extension
Distributed Near-Data Accelerator
Light-weight Locking Mechanism
Distributed Near-Data Accelerator
Useful Data in LLC
Too Many Instructions
Concurrency Overhead
Too Many Instructions
Useful Data in LLC
Concurrency Overhead

## Slide 16
X86-64 Instruction Extension
LOOKUP_B
  Behave like LOAD instruction.
  Return result to register directly.
LOOKUP_NB
  Behave like STORE instruction.
  Return result to the designated address.
SNAPSHOT_READ
  Read results from LOOKUP_NB instruction.
  Avoid cache line bouncing.
  Read snapshot of data without changing the
  cache line’s coherence state.
Low overhead
polling
Inputs: table address, key
Output: result (value)

## Slide 17
Experimental Setup
CPU model: Similar to Intel Xeon
  16 cores, 2.1GHz
  8-way 32KB L1D/I, 16-way 1MB L2 per core, 16-way 32MB shard LLC
Benchmarks: OVS + DPDK data plane
  Replaced hash-table lookup with HALO instructions
  Also evaluate TCAM
Power and area: CACTI and McPAT

## Slide 18
Throughput Benefit with HALO
~3x performance improvement with large tables.

## Slide 19
Scalability Benefit with HALO
HALO achieves good scalability with non-blocking mode.
More on-the-fly queries

## Slide 20
Energy Benefit with Halo
HALO is a cheap and energy-efficient design.
Cheap!

## Slide 21
Conclusion
Light-weight Locking Mechanism
X86-64 Instruction Extension
Distributed Near-Data Accelerator
Near data
Parallelism
Hw assisted
Low cost
All-in-one
Easy to use
Data Locality in LLC
Programmability
Concurrency Overhead

## Slide 22
Thanks!
Q&A